## Slide 1: Principles of a Grid Reference
To find the position of A:
1. Indicate the distance along the X axis (5)
2. Indicate the distance along the Y axis (8)
3. The combination of X-Y is the location of A. (5,8)
Y
Y
X
X
1 2 3 4 5 6 7 8
9 8 7 6 5 4 3 2 1
A
Level Three 419.03
OHP # 1

## Slide 2
Principles of a Grid Reference
Eastings and Northings
EASTING
N O R T H I N G
37
36
35
34
33
32
31
72 73 74 75 76 77
Eastings run from North to South. They are numbered from 00 to 99 and read from left to right.
Northings run from East to West. They are numbered from 00 to 99 and read from top to bottom.
Level Three 419.03
OHP # 2

## Slide 3: Order of Working a Grid Reference
1. The Easting is always the first half of the Grid Reference. This line forms the west side of the grid square.
2. The Northing is the second half of the GR. This line forms the south side of the grid square.
REMEMBER: In the house and up the stairs!!
Level Three 419.03
OHP # 3

## Slide 4: Four-Figure Grid Reference
Help Sgt Smith find tank!!!
46
45
44
43
42
26 27 28 29 30 31
32
Level Three 419.03
OHP # 4

## Slide 5: The Six-Figure Grid Reference
A 6-figure grid reference is a way of pinpointing a feature within a grid square.
It is accurate to within 100 meters and deals with 100m2 of ground.
A 6-figure GR is used when:
1. there are 2 or more of the same feature in a grid square, and
2. we need to be exact in giving a location.
Level Three 419.03
OHP # 5

## Slide 6: The Six-Figure Grid Reference
A 6-figure grid reference divides a grid square into 100 small squares.
Grid Square 7632 contains 5 bridges.
How will you know which one to go to?
Level Three 419.03
OHP # 6

## Slide 7: Taking A 6-Figure Grid Reference
Remember: “In the house, and up the stairs”
Bridge #1: 1 block east of 76, 6 blocks north of 32.
6-Figure GR for Bridge #1:
761326
Level Three 419.03
OHP # 7

## Slide 8: Use of a Romer
A romer is used to accurately measure a six-figure grid reference.
Place the corner of your paper on the landmark, and read off the 10ths.
Example: House
GR: 767328
Level Three 419.03
OHP # 8