## Slide 1: COMPASS BEARINGS
A compass bearing is a direction.
We measure bearings using
degrees (360o) or mils (6400).
Bearings are always measured
clockwise from North (zero line).
The magnetic declination
for your area must be set
on your compass before
taking a bearing!
North 0o
ANGLE
BEARING
Level Three 419.06
OHP # 1

## Slide 2: STEPS IN TAKING A COMPASS BEARING
1. Open the cover of the compass to about 50-70o.
2. Place the safety cord around your neck. Extend your arm and hold the compass flat at eye level.
3. Face the object. Use the sighting line in your compass to ensure that you keep all the parts in a straight line.
Level Three 419.06
OHP # 2

## Slide 3: STEPS IN TAKING A COMPASS BEARING (cont’d)
4. Turn the compass dial until the red end of the magnetic needle is inside the orienting arrow.
Remember: Do not look at the compass dial - look at its reflection in the mirror!
5. Open the cover and look at the number next to the luminous index pointer.
6. This number is your compass bearing!! You are ready to start hiking!!
Level Three 419.06
OHP # 3

## Slide 4: FOLLOWING A GIVEN BEARING
1. Turn the compass dial until the bearing appears opposite the luminous index pointer.
2. Place the safety cord around your neck and raise the compass to eye level.
3. Turn your body until the red end of the magnetic needle is lined up with the orienting arrow.
4. Look through the sight and select an object in your path.
5. Close the compass and hike to the object. When you reach it, choose a new landmark and repeat the steps.
Level Three 419.06
OHP # 4

## Slide 5: BACKBEARINGS
Backbearings are the opposite reading of a compass bearing.
To take a backbearing:
1. Read the number opposite the luminous point.
2. Turn the dial so that this number now appears at the luminous index pointer.
3. This new bearing will take you back to where you started
from!
St. John’s
Fredericton
Halifax
Level Three 419.06
OHP # 5